## Slide 1: Automated Solar Tracking System
19EEE381 – Open Lab Group No. - 06

## Slide 2: Team Members:
Krisshanth R – CB.EN.U4ELC22021
Praveenkumar U S - CB.EN.U4ELC22056
Aditya Thannasiappan - CB.EN.U4ELC22061
                Pranav Karthikeyan - CB.EN.U4ELC22062

## Slide 3: Table of contents 01 04 02 05 03 06
Problem Statement
Objective and Key features
Components List
Budget Estimation
Development Timeline (Week Plan)
Schematic Block Diagram

## Slide 4: Problem Statement
Stationary panels fail to follow the sun's movement
Lack of variable elevation angles affects efficiency
Commercial high-precision trackers are expensive and complex
Objective: Design a cost-effective dual-axis tracking system to improve energy capture
01

## Slide 5: Table of contents 01 04 02 05 03 06
Problem Statement
Objective and Key Features
Components List
Budget Estimation
Development Timeline (Week Plan)
Schematic Block Diagram

## Slide 6: Affordable and efficient dual-axis solar tracking system- Automated sun-tracking mechanism using LDR sensors- Real-time monitoring through OLED display and Blynk app- Utilizes ESP32 for communication and control Objective and Key Features
02

## Slide 7: Table of contents 01 04 02 05 03 06
Problem Statement
Objective and Key Features
Components List
Budget Estimation
Development Timeline (Week Plan)
Schematic Block Diagram

## Slide 8
03
Components List
S.No. | Components | Specification
1 | ESP-WROOM-32 | 2.4 GHz, Wi-Fi and Bluetooth, 3.6 V, 80mA
2 | Solar Panel | 6V, 100mAh
3 | LDR (LM393) Sensors | 10k Ohms. 3.3 - 5V
4 | Servo Motors (SG90) | Operating voltage: 3-7.2V
5 | OLED Display | 128x64 resolution, 5V DC
6 | CJMCU-219 INA219 Power Sensor | Voltage: 0-26V Current: 0-3.2A

## Slide 9: Table of contents 01 04 02 05 03 06
Problem Statement
Objective and Key Features
Components List
Budget Estimation
Development Timeline (Week Plan)
Schematic Block Diagram

## Slide 10: Budget Estimation
S.No. | Components | Cost
1 | ESP-WROOM-32 | Rs. 550
2 | Solar Panels (2 units) | Rs. 130
3 | LDR (LM393) Sensors (4 units) | Rs. 260
4 | Servo Motors (SG90) (2 units) | Rs. 400
5 | OLED Display | Rs. 270
6 | CJMCU-219 INA219 Power Sensor | Rs. 100
7 | 3D Model Printing | Rs. 800
Total Cost: |  | Rs. 2803
04

## Slide 11: Table of contents 01 04 02 05 03 06
Problem Statement
Objective and Key Features
Components List
Budget Estimation
Development Timeline (Week Plan)
Schematic Block Diagram

## Slide 12: Development Timeline (Week Plan)
W1: Topic decision and research discussion
W2: Cost estimation and report creation
W3: Hardware procurement and assembly
W4: Coding – Phase 1 (Wokwi simulation)
W5: Coding – Phase 2 and debugging (Arduino IDE)
W6: Implementation and testing
W7: Code optimization and model tuning
05

## Slide 13: Table of contents 01 04 02 05 03 06
Problem Statement
Objective and Key Features
Components List
Budget Estimation
Development Timeline (Week Plan)
Schematic Block Diagram

## Slide 14: Schematic Block Diagram
06

## Slide 15: Table of contents 06 09 07 10 08
Schematic Block Diagram
Testing and Wokwi Simulation
Results
Challenges Faced
Future Scope and Conclusion

## Slide 16: Testing and Wokwi Simulation
07

## Slide 17: Testing (Blynk web interface)
07

## Slide 18: Testing (Blynk App interface)
07

## Slide 19: Table of contents 06 09 07 10 08
Schematic Block Diagram
Testing and Wokwi Simulation
Implementation Results
Challenges Faced
Future Scope and Conclusion

## Slide 20: Implementation Results
Power Output Comparison
Fixed Panel: Less sunlight capture, lower energy
Single-Axis: Moves in one direction, ~30% more energy
Dual-Axis: Follows the sun, ~60% more energy
Data Logging & Analysis
Recorded power at intervals using sensors & IoT (Blynk app).
Compared energy output morning, afternoon, and cloudy days
Energy Gain Trends
Dual-axis gave the highest output.
Single-axis performed better than fixed panels.
Tracking helped even on cloudy days.
08

## Slide 21: Table of contents 06 09 07 10 08
Schematic Block Diagram
Testing and Wokwi Simulation
Implementation Results
Challenges Faced
Future Scope and Conclusion

## Slide 22: Challenges Faced
09
Sensor calibration issues
Debugging connectivity errors with ESP32
Stability concerns of procured 3D Model during swivel greater than 30°.
Stability issues faced when tested in extreme weather conditions.

## Slide 23: Table of contents 06 09 07 10 08
Schematic Block Diagram
Testing and Wokwi Simulation
Implementation Results
Challenges Faced
Future Scope and Conclusion

## Slide 24: Future Scope and Conclusion
10
Integration of AI for improved tracking precision.
Cloud-based data storage for advanced monitoring and analytics.
Expansion to larger solar arrays for industrial applications.
Conclusion:
Our system successfully enhances solar energy efficiency through a cost-effective dual-axis tracking mechanism.

## Slide 25: THANK YOU!